## Slide 1: The Summer of IP
SNAP Meeting
May 22, 2008

## Slide 2: Goals
Community (BSD) implementation of IP for tinyos-2.x
Implement the interesting parts of IP layer to enable research without going crazy
Explore centralized routing
Support future visibility research: wringer
Fix many things we don’t like

## Slide 3: Status
RFC4944 – faithful 6lowpan parser
On the mote: fragmentation, default route selection, forwarding, source routing
  Default route selection using IPv6 router solicitation/advertisement
  Source routing using compressed version of IPv6 “header type 0” source route
On the base: IPv6 driver, source routing/link state engine
Close to having “up the tree, down the tree” routing working & tested

## Slide 4: Thoughts…
We should like big packets – allows procrastination
Buffer management is key
Anycast from the base is easy; multicast may take some work
Parent selection well studied: parent switching policy not so much
Global network state seems achievable
Writing this stuff isn’t that hard! Making it work perfectly is the tricky part...

## Slide 5: Centralized Routing Myths (?)
Needs global topology information; nodes are scattered out of airplanes so that’s hard
  Network membership isn’t that dynamic
  Only need subset of single-hop table
  Updates only needed on demand
Latency is much worse in centralized routing
  Firstly, how important is that latency?
  Second, only control traffic should go through central points
Control traffic is excessive
  Can send control traffic only on demand, and only initial packet of flow

## Slide 6: Centralized Routing Advantages
Network Protocol Simplification
  Nodes only need to maintain a route to central router, and use forwarding table
Policy-Based Routing
  End user can easily experiment with various policies, i.e. opportunistic, energy based, etc.
Compact
  The right space complexity target is O(# flows)
  Reduce unnecessary control traffic
Scalable
  Larger networks can use multiple edge routers, which collectively maintain global network state